## Slide 1: Process Hazard Analysis For safe manufacturing
Inventys
10th January 2024

## Slide 2: Contents
Process Hazard Evaluation – Workflow
Hazard Identification
  Material Hazards
  Process Hazards
Hazard Characterization
Hazard Control and Addressal
Development Lifecycle vs. Hazard Evaluation

## Slide 3: Workflow – Process Hazard Evaluation @ Inventys
Hazards Identification
Literature
Hazard Characterization
Screening + Process Sensitivity Experiments
Process Safety Analysis
Identify Onset Temperatures [RM, INT, FG, RXN,WASTE]
MSDS
Exploratory Screening Experiments
Thermal Stability Analysis (DSC/TSU) [RM, INT, FG]
Specific Heat Estimation
Reaction Heat Estimation (Calorimetry vs. Analog Calculation)
Side/Decomposition Chemistry Evaluation
Evaluation of MTSR, Onset Temperatures vs. MTT
Rate, Profile of Temperature and Pressure Increase
Hazard Addressal (Safety Measures)
Optimize and Set Process Parameters (T, P, Order Addition, Conc., Solvent etc.)
Automation and Safety Interlocks
Thermal Stability Analysis (DSC/TSU) [RXN,WASTE]
Engineering Design Requirements (Utility Load/Type, Vent Sizing, MoC, Scrubber / Vent Design)
Formation of known non-condensable or toxic species (based on Chemistry)
Peak Gas Formation Rate
QC/Analysis, Instrumentation around Critical Parameters
HAZOP

## Slide 4: Hazard Categories – What do we look for
Hazards associated with the chemical operations under consideration are categorized as
Material-related Hazards
  Related to properties associated with the materials being used in the process
  Reactants, products, intermediates, reagents, solvents, catalysts
    Toxicity
    Flammability
    Material Incompatibility
    Corrosivity
    Volatility
    Physicochemical Stability
    Dust/Powder Properties (related to solids)
Process-related Hazards
  Related to the chemistry of each material under the relevant process conditions, and wanted or unwanted interactions between the materials involved in the process
    Exothermicity
    Formation of Non-Condensable/Volatile Species
    Nature of side products
      Toxicity, Stability

## Slide 5: Hazard Characterization – Material Hazards
Toxicity
Flammability
Material Incompatibility
Corrosivity
  Safety Data Sheet
  Chemistry knowledge of relevant functional groups
  Laboratory experiments (ex. Coupon test)
    For Corrosivity
Volatility
Chemical Stability
  Safety Data Sheet
  Properties of similar compounds
  DSC (heat, pressure vs. temperature)
  Stability Studies
    Related to stability of RM, INT, FG across boundaries of normal operating conditions
      Time, Temperature, Humidity
Dust/Powder Properties (related to solids)
  MIE (dust cloud, without inductance)
  Dust Explosivity
  Falling Hammer

## Slide 6: Hazard Characterization – Process Hazards
Thermal Hazards (Exotherm)
  Literature/Chemistry Knowledge
  Estimation of reaction heat using simplified analogs
    Where possible
  Screening experiments  profile and magnitude of exotherm
  DSC Evaluation (T vs. W)
    Raw Materials, Reagents, Intermediates, FG
    Reaction Mass
      Before Reaction (t0)
      Mid Reaction  transient thermal hazards
      After Reaction (tf)  residual thermal hazards
Pressure Hazards (Release of Non-Condensable/Volatile Species)
  Literature/Chemistry Knowledge
  Material Properties (volatility, thermal/chemical stability)
  TSU Evaluation (T vs. P)
    Raw Materials, Reagents, Intermediates, FG
    Reaction Mass
      Before Reaction (t0)
      Mid Reaction  transient thermal hazards
      After Reaction (tf)  residual thermal hazards

## Slide 7: How are identified hazards addressed?
Identified process hazards will influence several or all aspects of the production cycle
  Material Storage and Handling
  Reaction Operations
    Operating parameters
    In-process specifications
  Work-Up / Isolation Operations
  Effluent Treatment
Hazards are addressed by
  Engineering Design
    Facility/equipment features to either prevent, mitigate, or allow for safe resolution of process hazards
  Process Automation
    Control loops around critical operations or process parameters
  Process Chemistry
    Parameter control optimization to minimize risk associated with potentially hazardous operations
    Route Design / Reagent Selection for inherently safer operation
  Quality Control
    To ensure key process parameters and quality specifications are being followed
  Training  Behavioral Control
    To ensure that all relevant personnel are aware of the risks of an operation and how to operate in a safe manner

## Slide 8: Workflow – Development Lifecycle vs. Hazard Evaluation
Preliminary Feasibility Studies
(Route Selection)
MSDS Review
Development and Optimization
(Fixed Route, Sample)
Further Screening / Sensitivity trials (lab)
Laboratory Scale-Up
(Kilo)
Set Operating Parameters (T,P, Order Addition, Conc.) considering Reaction Heat, Onset Temperatures
Chemistry / Structure Review  Material / Process Hazards
Screening / Sensitivity Experiments (partial characterization)
DSC/TSU analysis (known hazards)
Thermal stability analysis DSC/TSU [RM,INT, FG, RXN, WASTE]
Specific Heat, Reaction Heat Estimation (Calorimetry, Analog Calculation)  MTSR vs. MTT
Evaluate Peak Gas Formation (amount, rate, profile  peak)
Literature Review
Pilotation
Side/Decomposition Chemistry Evaluation
Set Handling and Containment Methodology for Scale (Toxicity, Flammability, vs. Phys Prop.)
Identification of Critical Process Parameters
HAZOP 1  Pilot Modifications  BMR Drafting (safety, critical operations, parameters)  Training
If Available: Reaction Calorimetry (for critical reactions)
Process Mapping to Pilot
Validate/update data based on pilot observations (engineering design/ calculations, process parameters)
Engineering Calculations (Heat Load, Scrubber Load etc.
Automation / Control Loops for identified critical process parameters and operation
BMR Drafting (with information on material safety and critical process parameters/operations)
Process revision (as required)
HAZOP 2  Plant Modifications, Safeguards, Automation  Re-training
Commercial Production
(Before)
BMR Re-drafting
PID based on HAZOP 2
Facility Modification (as necessary)
Powder Safety Studies
Re-training
HIRA